## Slide 1: HNF 150S-160S Compact Efficiency @ Value
2022.10.19, Sunny Xu, SOCMA China

## Slide 3: SOCMA compact 15-16ton forklift series
H N F 150 - S
Origin from SOCMA’s Chinese name”HUA NAN”
Origin from SOCMA’s Chinese name”HUA NAN”
Product range
HNF 150S-160S Compact
HNF150S
Rated Capacity 15000kg@600mm
HNF160S
Rated Capacity 16000kg@600mm
Diesel
Rated Carrying Capacity 15ton
“Small” type-compact
Model description
3
HNF150S-160S Standard | Sunny Xu | Q1 2022

## Slide 4: SOCMA compact 15-16ton forklift series
Lowered Mast Height 3150-4400mm
Lifting or Lowering speed with/without load lifting: 0.205-0.255m/s
lowering: 0.435-0.285m/s
Mast Lift Height 3000-5500mm
Turning radius 4750mm
[ varies depending on model]
Travel speed 23.0~26.0km/h
[ varies depending on model and load]
Load capacity 15-16T
[ varies depending on model and mast]
Climbing ability with/without load 20/22%
4
HNF150S-160S Standard | Sunny Xu | Q1 2022
HNF 150S-160S Compact

## Slide 5: SOCMA compact 15-16ton forklift series
ACTION POWERFUL
MOVING FAST
OPERATION SENSITIVE
USING DURABLE
For efficient and safe handling
HNF 150S-160S Compact

## Slide 6: SOCMA compact 15-16ton forklift series
OPERATES IN TIGHT SITUATIONS
the steering axle has small turning radius hanks to 3300 mm wheelbase
EFFORTLESS MAINTENANCE
with tilting cab
OPERATED AT LOW COST
through low fuel consumption and predictable maintenance
HNF 150-160 Compact
REMARKABLE VISIBILITY
with wide view cabin

## Slide 7: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
Load capacity

## Slide 8: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
Data Sheet
SOCMA 16-тонный компактный дизельный вилочный погрузчик |  |  | 
Модель | - | HNF160S | 
Тип силовой установки | - | Дизель | 
Грузоподъемность | кг | 16000 | 
Центр груза | мм | 600 | 
Тип привода | - | 2WD | 
Размеры |  |  | 
Высота подъема | мм | 3000 | 
Размеры вил (Д*Ш*В) | мм | 1200*180*90 | 
Угол наклона мачты (вперед/назад) | Градусы | 6/12 | 
Ширина каретки вил | мм | 2200 | 
Общая длина (без вил) | мм | 5155 | 
Общая ширина | мм | 2400 | 
Высота мачты | мм | 3140 | 
Высота козырька крыши | мм | 3040 | 
Клиренс (рамы) | мм | 225 | 
Минимальный радиус поворота | мм | 4750 | 
Колесная база | мм | 3300 | 
Колея передних колес | мм | 1740 | 
Колея задних колес | мм | 2013 | 
Собственный вес | мм | 19800 | 

## Slide 9: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
Рабочие характеристики |  |  | 
Максимальная скорость (с грузом/без груза) | км/ч | 23/26 | 
Скорость подъема вил (с грузом/без груза) | мм/с | 205/255 | 
Скорость опускания вил (с грузом/без груза) | мм/с | 435/285 | 
Способность преодолевать подъем (с грузом/без груза) | Градусы | 20/22 | 
Шины |  |  | 
Передние шины | - | 12.00-20-18PR | 
Задние шины | - | 11.00-20-18PR | 
Тип шин | - | Пневматические шины | 
Количество шин (перед/зад) | шт. | 4/2 | 
Двигатель и трансмиссия |  |  | 
АКБ | В/А/ч | 2х12/90 | 
Производитель двигателя |  | Dongfeng Cummins | 
Модель двигателя |  | National III QSB4.5-C130 | 
Номинальная мощность двигателя | кВт/об.мин. | 97/2200 | 

## Slide 10: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
5.5 | Номинальный крутящий момент | Н*м/об.мин. | 418/1500
5.6 | Количество цилиндров | шт. | 4
5.7 | Рабочий объем двигателя | л | 4,5
5.8 | Рабочее давление навесного оборудования | МПа | 16
5.9 | Рабочий поток масла при использовании навесного оборудования | л/мин. | 40
5.10 | Трансмиссия |  | 2/2 Power Shift
5.11 | Тип трансмиссии |  | Трансмиссия с гидравлической муфтой

## Slide 11: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
Chassis
This is subjected to Finite Element Analysis(FEA) to ensure that there is always enough safety margin under severe working conditions; the workmanship is exquisite and firm. Effectively alignment with axles and transmission to ensure the lateral and longitudinal stability and energy saving of the entire vehicle operation process
Box type chassis
Strong welded structure
Anti-slip steps
Good rigidity and strength

## Slide 12: SOCMA compact 15-16ton forklift series
Drivetrain
HNF 150S-160S Compact
Engine-well-known turbocharged engine: strong horsepower, large torque reserve, low fuel consumption, high reliability; easy access to accessories
Yuchai YC6J150-T301
Dongfeng Cummins 6BT5.9-C130 CN2
Dongfeng Cummins QSB4.5-C130 Euro III
Transmission-automatic shift transmission can change gears very smoothly, reliable, safe, and easy to maintain.
2 FW/2RW
Drive axle-adopts a heavy-duty forklift drive axle
Large load capacity
Long service life
Heavy duty Air filter

## Slide 13: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
Hydraulic System
Double pumps merge, steering priority hydraulic system
Equipped with oil return radiator and back pressure protection device to ensure the heat balance of the whole machine.
Single-handle joystick control valve and electronically controlled variable speed control valve, make operation of the whole machine lighter and more flexible
Full hydraulic steering priority system, with effortless action and control

## Slide 14: SOCMA compact 15-16ton forklift series
Controls
HNF 150-160 Compact
Pilot valve control device to make the work efficient and reduce drivers’ labor intensity.
Joystick controlled mast and carriage operation.
Drive direction controlled lever on steering column
Operator’s color display indicator 6”
Engine RPM, Temperature, Fuel level, Working hours
Drive direction FNR
Brake system air pressure & hydraulic oil pressure
Optional load indicator & printer

## Slide 15: SOCMA compact 15-16ton forklift series
Cabin
HNF 150S-160S Compact
Sliding windows L / R
Doors both sides
Wipers
  Front, rear
Heating system
Air conditioning system
Suspended frame, comfortable and spacious.
Seat front /rear and height adjustable
Wheel column angle is adjustable
At glance controls and display
Operator’s presence system optional

## Slide 16: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
Lifting height
  3m duplex as standard
  3-5.5m as option
Lifting speed
0.205m/s- 0.255m/s with full load/without load
Lowering speed
0.435m/s-0.285m/s without load/with full load
Mast
Box-type internal-external mast, special all-round roller bearings, increase lifting performance

## Slide 17: SOCMA compact 15-16ton forklift series
Free Mast
HNF 150S-160S Compact
Lifting height
  3m duplex wide view type as standard
  3-5.5m duplex/triplex free mast as option
  Freelift 998-1833mm as option
Lifting speed
0.205m/s- 0.255m/s with full load/without load
Lowering speed
0.435m/s-0.285m/s without load/with full load

## Slide 18: SOCMA compact 15-16ton forklift series
HNF 150S-160S Compact
Carriage
Strong and durable construction, tested through Finite Element Analysis(FEA), it can resist high intensity operations.
Durable & robust design
Full stroke
Standard with fork positioner and side shifter
Optional design for stone and mining application

## Slide 19: SOCMA compact 15-16ton forklift series
Forks
HNF 150S-160S Compact
Standard dotation
  1200x180X90
CASCADE brand, stronger, more wear-resistant,
Optional with alternative customized lengths
Quick interchangeable and replaceable

## Slide 20: SOCMA compact 15-16ton forklift series
Maintenence
HNF 150S-160S Compact
Easy access to preventive maintenance components
Engine hood with assisting pneumatic spring
Cabin can be tilted to the right for maintenance access

## Slide 21
THANK YOU!
Notes: Chart layout »Chapter chart«